# Text boxes

# DELIVERY METHOD STATEMENT

# SEQUENCE OF EVENTS

- Upon arrival & prior to commencing work activity, our personnel to report to THE HIRER responsible site person(s) or their representatives (s)

- HIRER personnel to ensure Flintham Contractors / employees obtain site induction, permits to work. Lorry loader operative to wear appropriate PPE, as instructed at all times

- When acceptance of the Method Statement is agreed with HIRER, the lorry loader operator/lifting supervisor will request information on the required loading/landing position for the office/container to be placed

- Lorry loader will then drive to the requested area and position vehicle adjacent to the nominated area (Should any reversing be involved with this procedure the HIRERS is responsible for providing a person to aid the lorry loader operator, particularly when the reversing procedure involves confined/blind movements)

- Lorry loader operator will then set up the lorry loader as per the manufactures instructions. Suitable supports will be placed under the outriggers where indicated by the clients Method Statement (Ground conditions are the responsibility of the HIRER and all necessary preparation should be considered prior to lorry loaders arrival on site)

- Lorry Loader Operator will raise crane and position so as attached “o” ring of lifting chains and inertia reel fall block to crane hook

- Lorry Loader Operator will raise crane and position over the centre of the office/container unit and by use of stabilised ladder will attach lifting hooks to unit by positioning ladder at each lifting point. Operator will alight from ladder. (A safety harness is available should roof access be required and will be attached to the inertia reel fall block)

- A guideline is to be attached to the unit to assist in controlling potential unit swing. ( Hirer to provide person to control guideline)

- The crane hook will now be raised to take weight of the load and ensure that lift is centred. Load is then slewed over final position and lowered into place

- When crane operation complete the lorry loader operator will remove lifting tackle from crane hook by accessing lifting points at roof level of office/container by use of ladder, as per section 7 above.

- After the four legs of the lifting tackle are removed lorry loader operator will raise crane slew towards bed of lorry loader, remove lifting tackle and stow crane. Operation is now complete

- Repeat lifts will follow sections 4 through 10 as above

- Lorry loader is removed from site under HIRER instructions

### DELIVERY METHOD STATEMENT APPROVAL

Originator : Flintham Cabins Ltd              Hirer:

Name: John Lilly	         Name:

Date: