# Text boxes

# ACTIVITY

#### USE OF LADDER

Fall from height whilst attaching / detaching lifting gear

WORKING AT HEIGHT

Walking on Cabin roof, no edge protection

NON-ESSENTIAL PERSONNEL / PUBLIC INTERFACE

Object falling onto or striking persons not involved in lifting operation

Frequency X Severity Xcontrol Rating = Risk Rating+

2 x 4 x 0.5 = 4

2 x 5 x 0.5 = 5

2 x 3 x 0.75 = 4.5

##### COMMENT

Follow Method Statement. Ladder to be in good order and inspected prior to use. Ladder to be footed or stabiliser attached.

Over reaching to be avoided.

Check for proximity of electric cables as aluminium ladders should not be used in vicinity of.

Persons to wear a body harness and shall clip on lanyard to inertia reel fall block where there is no provision of edge protection. Preferably avoid roof access by locating ladder at each lifting point

ACCESSING ROOF IS LAST RESORT – POSITIONING LADDER AT EACH LIFTING POINT IS PREFERRED METHOD

Persons not involved in lifting operation should be controlled so that they do not encroach into lifting radius. HIRER responsibility. Control methods are cordoning off working area for unauthorised encroachment.