# Text boxes

# ACTIVITY

#### USE OF LORRY LOADER

*Failure of equipment

*Overturning due poor ground

*Over turning due to component failure

*Striking of adjacent / overhead obstructions/cables

*Other proximity hazards

.

Frequency X Severity Xcontrol Rating = Risk Rating+

2 x 4 x 0.5 = 4

##### COMMENT

Operator to use equipment as per manufactures instructions. Have currant CTA and relative test certification available for inspection

Operator will examine ground surface prior to lifting operation (Ground conditions are HIRER responsibility)

Visual inspection of vehicle and crane are to be undertaken by operator prior to any lift.

Visual inspection of lifting area to be carried put by operator prior to commencement of operation

Check for proximity hazards.

###### DELIVERY METHOD STATEMENT APPROVAL

Originator:  Flintham Cabins Ltd                 Hirer:

Name: John Lilly                                              Name:

Date: