TRANSPORT METHOD STATEMENT

Delivery/Collection/Movement of

Cabins/Containers/Associated Equipment

This Method Statement has been produced to comply with the Health & Safety at Work Act 1974 and BS7121 Safe use of Cranes Part 4:2010 - Lorry Loaders to provide a Safe System of Work for the installation and removal of Cabins/Containers and associated equipment.

| Client: |  |
| --- | --- |
| Project: |  |
| Site Address: |  |
| Site Contact Name: |  |
| Telephone: |  |
| Job Date: |  |
| Haulage Contractor: |  |
| Emergency Contact: |  |
| Emergency Contact No: |  |
| Scope of Works: Use of Lorry Loader to deliver/collect to/from site Unit Weight: Will vary for each unit, but will not exceed the heaviest which is 3500kgs (amend as necessary) |

The operator of the lorry loader is also given absolute authority to STOP the lifting operation if he/she considers that a danger is likely to arise if the operation were to continue.

General Conditions:

All drivers/Haulage Contractors operating on behalf of Flintham cabins Ltd must wear the following mandatory items of PPE;

- Safety Gloves

- Safety Hard Hat

- Hi-visibility Jacket / Vest

- Safety shoes/boots with 200 joule toecap and midsole

- Safety Harness and Fall Arrest Block when working at height

All equipment for the lifting operation is provided by the Haulier and tested and inspected under the Provision and Use of Work Equipment Regulations 1998 (PUWER) and The Lifting Operations and Lifting Equipment Regulations 1998.

##### Site Events – Controls Required

- On arrival at the site the driver must report to the client or the client’s representative. Sign in and liaise with the client regarding site safety arrangements and be prepared undertake a site induction if required.

- Discuss arrangements for positioning of cabin, container or other associated equipment with the client. Details contained within this Method Statement and Risk Assessment must be discussed and agreed, and site-specific information completed if required.

- Once the exact position for the cabin, container or other associated equipment is known the driver will    proceed to the loading/unloading point.

- Siting the Lorry loader must take account of all the factors that may affect its safe operation, particularly the following;

  - Height and width restrictions - telephone lines / tree canopy’s etc…

  - Proximity hazards such as parked vehicles and building projections.

  - Ground conditions in the loading / unloading area.

  - Underground services, drains, culverts and manhole covers.

- When satisfied that all obstacles have been identified and addressed the lorry loader can be set up in accordance with the manufacturer’s instructions, generally in accordance with the following procedure.

  - The operator will manoeuvre the vehicle in to position adjacent to the final position of the unit.

  - Marker boards, flashing lights, securing straps, chains or other restraints will all be removed from the unit.

  - Steadying ropes will be attached to the load if required to ensure the operator has full control of the unit during the lifting operation

  - Stabilisers will be extended, and ground mats positioned under the stabilisers to protect the ground surface.  Whilst all reasonable care will be taken to protect the ground surfaces, we cannot be responsible for unstable ground conditions resulting in damage to tarmac or underground duct, drains, manhole covers etc.

##### Lifting Procedure

- The lorry loader will be unfolded in accordance with the manufacturers operating instructions and a suitable 4-leg chain set complete with shortening clutches and a fall arrest reel with tag line will be fitted to the lorry loader hook.

- Detail as to the exact chain length required achieving the optimum 90o lifting angle can be found in the appropriate technical specification chart in the Drivers Manual.

- The operator will slew the chains above the unit and lower them over the centre of the load.

- The operator will use a suitable ladder, to access the roof of the unit if required. The ladder should be tied or footed whilst the operator mounts/dismounts and extends at least 1m above the roof of the unit to provide a secure handhold. In accordance with guidance on the Safe use of Ladders & Stepladders INDG402.

- The operator will attach the fall and arrest cable to the lanyard on their harness before ascending ladder and proceed to attach each leg of the chain set to the lifting point on the unit.

- Once the chains are connected the operator will descend the ladder and detach the fall-arrester.

- The ladder is removed clear of the load and vehicle.

- The operator ensures that all personnel are clear of lifting zone and that there are no other obstructions.  If the lifting area is clear the lifting operation can commence.

- The operator under control will slowly commence the lifting operation, ensuring that tension is taken up evenly on all chain legs, ensuring the master link is in a vertical position looking from all angles.

- The operator slowly lifts unit and manoeuvres the unit at low level to its resting point, under guidance from site assistance.

Under BS7121 Safe use of Cranes 2010: Part 4 Lorry Loaders; The operator of the lorry mounted crane is also given authority to STOP the lifting operation if he/she considers that a danger is likely to arise if the operation were to continue.

- Delivery of cabins/containers only: - The unit is then lowered to ground; the unit is levelled using a spirit level and shims to ensure the doors open and close freely.

- Delivery of cabins/containers only: - When the operator is happy that the unit is level the lorry loader is lowered to release all tension on chain legs.

- Repeat Steps 4, 5 and 6.

- The operator removes the ladder clear of the unit retracts the extensions and stores ladder on lorry.

- The operator lifts the lorry loader to raise chains from top of unit, manoeuvres to remove chains, which are detached and stored away.  The lorry loader can now be folded away as per the manufacturer’s instructions.

- Stabilisers are fully retracted, ground mats stowed on the vehicle. PTO is disengaged ensuring the vehicle is fit to travel off site.

- Guide ropes can now be removed from the unit and stowed on the vehicle.

- The operator ensures the client is satisfied with the installation/removal handing over or collecting the unit keys and gaining a clear name and signature on the proof of delivery paperwork provided by us.

The vehicle will leave site.

##### Site Specific Information

List any other factors that are specific to the site and provide resolution.

| SITE ACCESS | Clear access |  | Restricted width | Mtrs | Restricted Height | Mtrs |
| --- | --- | --- | --- | --- | --- | --- |
|  | Parked vehicles |  | Site Restrictions |  |
| ACCESS ROAD | Hard |  |  |  | TRAFFIC MANAGEMENT Required? |  | If Yes, specify |
| WORK AREA | Hard |  |  |  | Attention required* |  | If Yes, specify |
|  | Underground Services |  | Specify: |
| GROUND CONDITIONS | Good |
| OVERHEAD OBSTRUCTION | Bare power cables |  | Other power cables |  | Telephone cables |  |
|  | Overhanging trees |  | Other – specify |  | Max. Headroom |  |
| Other considerations |  |

Site Drawing (if required)

I/we confirm all necessary arrangements for the installation of the above building(s) and safety requirements have been identified.

| Client Signature: |  |  | Signed on Behalf of Haulier: |
| --- | --- | --- | --- |
| Print Name: |  |  | Print Name: |  |
| Date: |  |  | Date: |  |

# Text boxes

FLINTHAM CABINS LTD

Tel: 0208 459 6972

Email: john@flinthamcabins.com